## Slide 1: Hydrologic Information Systems to discover and combine data from multiple sources for hydrologic analysis
David Tarboton
Utah State University
Support
EAR 0622374
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/

## Slide 2
What proportion of your research time do you spend on preparing or preprocessing data into appropriate forms needed for research purposes?
http://his.cuahsi.org/documents/HISStatusSept15.pdf
Chart: 
| < 10 % | 10-25 % | 25-50 % | 50-75 % | > 75 % None
 | 18.6 | 45.7 | 24.3 | 11.4 | 0
Notes: Surveys of the hydrology community have indicated that data gathering and preprocessing is an inordinate fraction of the time required for modeling and analysis
In hydrology most of the easy single site, single variable, low hanging fruit research problems are solved and advances in understanding and better predictions require
combining information from multiple sources,
sharing and collaboration
Easier access to advanced computational capability
Sustainability and reliability in software

## Slide 3: CUAHSI HIS
HydroServer – Data Publication
Lake Powell Inflow and Storage
HydroDesktop – Data Access and Analysis
HydroDesktop – Combining multiple data sources
HydroCatalog
Data Discovery
The CUAHSI Hydrologic Information System (HIS) is an internet based system to support the sharing of hydrologic data. It is comprised of hydrologic databases and servers connected through web services as well as software for data publication, discovery and access.

## Slide 4: The CUAHSI Hydrologic Information System Team
University of Texas at Austin – David Maidment, Tim Whiteaker, James Seppi, Fernando Salas, Jingqi Dong, Harish Sangireddy
San Diego Supercomputer Center – Ilya Zaslavsky, David Valentine, Tom Whitenack, Matt Rodriguez
Utah State University – David Tarboton, Jeff Horsburgh, Kim Schreuders, Stephanie Reeder
University of South Carolina – Jon Goodall, Anthony Castronova
Idaho State University – Dan Ames, Ted Dunsford, Jiří Kadlec, Yang Cao, Dinesh Grover
Drexel University/CUNY – Michael Piasecki
CUAHSI Program Office – Rick Hooper, Yoori Choi, Jennifer Arrigo, Conrad Matiuk
ESRI – Dean Djokic, Zichuan Ye
Users Committee – Kathleen Mckee, Jim Nelson, Stephen Brown, Lucy Marshall, Chris Graham, Marian Muste
Support
EAR 0622374
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/

## Slide 5
CUAHSI is a consortium representing 125 US universities (plus international affiliate members)
Supported by the National Science Foundation Earth Science Division
Advances hydrologic science in nation’s universities
Projects in Informatics, Instrumentation, Observatories, Synthesis, and Research Applications
http://www.cuahsi.org
What is CUAHSI?

## Slide 6: Hydrologic Data Challenges
From dispersed federal agencies
From investigators collected for different purposes
Different formats
  Points
  Lines
  Polygons
  Fields
  Time Series
Rainfall and Meteorology
Water quantity
Soil water
Groundwater
Water quality
GIS
Data Heterogeneity
The way that data is organized can enhance or inhibit the analysis that can be done

## Slide 7: The way that data is organized can enhance or inhibit the analysis that can be done
I have your information right here …
Picture from: http://initsspace.com/

## Slide 8: Hydrologic Science
Hydrologic conditions
(Fluxes, flows, concentrations)
Hydrologic Process Science
(Equations, simulation models, prediction)
Hydrologic Information Science
(Observations, data models, visualization
Hydrologic environment
(Physical earth)
Physical laws and principles
(Mass, momentum, energy, chemistry)
It is as important to represent hydrologic environments precisely with
data as it is to represent hydrologic processes with equations

## Slide 9: Data models capture the complexity of natural systems
NetCDF (Unidata) - A model for Continuous Space-Time data
Space, L
Time, T
Variables, V
D
Coordinate
dimensions
{X}
Variable dimensions
{Y}
ArcHydro – A model for Discrete Space-Time Data
Space, FeatureID
Time, TSDateTime
Variables, TSTypeID
TSValue
Terrain Flow Data Model used to enrich the information content of a digital elevation model
CUAHSI Observations Data Model: What are the basic attributes to be associated with each single data value and how can these best be organized?

## Slide 10
Data Searching – What we used to have to do
NWIS
NARR
NAWQA
NAM-12
request
request
request
request
request
request
request
request
return
return
return
return
return
return
return
return
Searching each data source separately
Michael Piasecki
Drexel University
Notes: 10

## Slide 11
What HIS enables
Searching all data sources collectively
NWIS
NAWQA
NARR
generic
request
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
ODM
Michael Piasecki
Drexel University
Notes: 11

## Slide 12: Video Demo
http://his.cuahsi.org/movies/JacobsWellSpring/JacobsWellSpring.html

## Slide 13: Web Paradigm
Catalog (Google)
Web Server
(CNN.com)
Browser
(Firefox)
Access
Catalog harvest
Search

## Slide 14: CUAHSI Hydrologic Information System Services-Oriented Architecture
Data Discovery and Integration
Data Publication
Data Analysis and Synthesis
HydroCatalog
HydroDesktop
HydroServer
ODM
Geo Data
Data Services
Metadata Services
Search Services
WaterML, Other OGC Standards
Information Model and Community Support Infrastructure

## Slide 15: What are the basic attributes to be associated with each single data value and how can these best be organized?
Space, S
Time, T
Variables, V
s
t
Vi
vi (s,t)
“Where”
“What”
“When”
A data value
Variable
Method
Quality Control Level
Sample Medium
Value Type
Data Type
Source/Organization
Units
Accuracy
Censoring
Qualifying comments
Location
Feature of interest
Latitude
Longitude
Site identifiers
DateTime
Interval (support)

## Slide 16: Observations Data Model (ODM)
Soil
moisture
data
Streamflow
Flux tower data
Groundwater
levels
Water Quality
Precipitation
& Climate
A relational database at the single observation level
Metadata for unambiguous interpretation
Traceable heritage from raw measurements to usable information
Promote syntactic and semantic consistency
Cross dimension retrieval and analysis
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment, and I. Zaslavsky (2008), A relational model for environmental and water resources data, Water Resources Research, 44, W05406, doi:10.1029/2007WR006392.
Provides a common persistence model for data storage

## Slide 17
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment and I. Zaslavsky, (2008), A Relational Model for Environmental and Water Resources Data, Water Resour. Res., 44: W05406, doi:10.1029/2007WR006392.
CUAHSI Observations Data Model http://his.cuahsi.org/odmdatabases.html
Notes: In designing ODM we asked: What are the basic attributes to be associated with each single data value and how can these best be organized? This involved community survey at a workshop and by email and based on the feedback received we came up with the ODM schema illustrated, published last year in WRR
This is quite a detailed slide, but it is the entire schema. Few database designs are simple enough to fit the entire schema on one slide. This shows at the center the data values table and off to the sides, the ancillary or metadata tables that record.

## Slide 18: Discharge, Stage, Concentration and Daily Average Example

## Slide 19: Site Attributes
SiteCode, e.g. NWIS:10109000
SiteName, e.g. Logan River Near Logan, UT
Latitude, Longitude Geographic coordinates of site
LatLongDatum Spatial reference system of latitude and longitude
Elevation_m Elevation of the site
VerticalDatum Datum of the site elevation
Local X, Local Y Local coordinates of site
LocalProjection Spatial reference system of local coordinates
PosAccuracy_m Positional Accuracy
State, e.g. Utah
County, e.g. Cache

## Slide 20
Feature
Waterbody
HydroID
HydroCode
FType
Name
AreaSqKm
JunctionID
HydroPoint
HydroID
HydroCode
FType
Name
JunctionID
Watershed
HydroID
HydroCode
DrainID
AreaSqKm
JunctionID
NextDownID
ComplexEdgeFeature
EdgeType
Flowline
Shoreline
HydroEdge
HydroID
HydroCode
ReachCode
Name
LengthKm
LengthDown
FlowDir
FType
EdgeType
Enabled
SimpleJunctionFeature
1
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
*
1
*
HydroNetwork
*
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
1
1
CouplingTable
SiteID
HydroID
Sites
SiteID
SiteCode
SiteName
Latitude
Longitude
…
Observations Data Model
1
1
OR
Independent of, but can be coupled to Geographic Representation
ODM
e.g. Arc Hydro

## Slide 21: Stage and Streamflow Example
Notes: Discharge Derived from Gage Height
Concepts:
Data derived from other data – single data point derived from a single observation (discharge from stage)
Data derived using a specific method (discharge from stage using rating curve)
Relationships:
Relationships between Values table and DerivedFrom table on DerivedFromID and ValueID
Relationship between Values table and Variables table on VariableID
Relationship between Values table and Methods table on MethodID
Relationship between Variables table and Units table on UnitID

## Slide 22: Water Chemistry from a profile in a lake
Notes: Water Chemistry From a Lake Profile
Concepts:
Grouped observations (all observations in one reservoir profile)
Observations made using an offset (observations made at multiple depths below the surface of a reservoir)
Observations made using a specific method (observations made using a particular field instrument)
Relationships:
Relationship between Values table and the Variables table on VariableID
Relationship between Values table and OffestTypes table on OffsetTypeID
Relationship between Values table and Methods table on MethodID
Relationship between Variables table and Units table on UnitID
Relationship between GroupDescriptions table and Groups table on GroupID
Relationship between OffsetTypes table and Units table on UnitID and OffsetUnitID

## Slide 23: Loading data into ODM
Interactive OD Data Loader (OD Loader)
  Loads data from spreadsheets and comma separated tables in simple format
Scheduled Data Loader (SDL)
  Loads data from datalogger files on a prescribed schedule.
  Interactive configuration
SQL Server Integration Services (SSIS)
  Microsoft application accompanying SQL Server useful for programming complex loading or data management functions
OD Data Loader
SDL
SSIS

## Slide 24: Importance of the Observations Data Model
Provides a common persistence model for observations data
Syntactic consistency (File types and formats)
Semantic consistency
  Language for observation attributes (structural)
  Language to encode observation attribute values (contextual)
Publishing and sharing research data
Metadata to facilitate unambiguous interpretation
Enhance analysis capability

## Slide 25
Set of query functions
Returns data in WaterML
WaterML and WaterOneFlow
WaterML is an XML language for communicating water data
WaterOneFlow is a set of web services based on WaterML
GetSites
WaterOneFlow
Web Service
GetValues
GetSiteInfo
GetVariableInfo
Notes: 25

## Slide 26
http://www.opengeospatial.org/standards/waterml
Open Geospatial Consortium Web Service Standards
This document is an OGC® Encoding Standard for the representation of hydrological observations data with a specific focus on time series structures.
These standards have been developed over the past 10 years …. by 400 companies and agencies ....

## Slide 27
Feature of Interest
Procedure (ID := “DAVIS_123“)
23 m/s 16.9.2010 13:45
Result
uom
Sampling Time
Observed Property := “Wind_Speed“
Observation
Sensor Observations Service: Get Observation
Notes: Basis for a standardized access to sensor data is the observation model defined in the Observations & Measurements standard. Let me briefly describe the main concepts / terms used in this model…

## Slide 28: HydroServer – Data Publication
Ongoing Data Collection
Data presentation, visualization, and analysis through Internet enabled applications
Internet Applications
Point Observations Data
Historical Data Files
GIS Data
ODM Database
GetSites
GetSiteInfo
GetVariableInfo
GetValues
WaterOneFlow
Web Service
WaterML
OGC Spatial Data Service from ArcGIS Server
Notes: A platform for publishing space-time hydrologic datasets that:
  Autonomous with local control of data
  Part of a distributed system that makes data universally available
Basis for Experimental Watershed or Observatory data management system
Standards based approach to data publication
  Accepted and emerging standards for data storage and transfer (OGC, WaterML)
Built on established software
  MS SQL Server, ArcGIS server
Open Source Community Code Repository
  Sustainability

## Slide 29
HydroCatalog
GetSites
GetSiteInfo
GetVariableInfo
GetValues
WaterOneFlow
Web Service
WaterML
Discovery and Access
Hydro
Desktop
Water Metadata Catalog
Harvester
Service Registry
Hydrotagger
Search Services
http://hiscentral.cuahsi.org
Search over data services from multiple sources
Supports concept based data discovery
CUAHSI Data Server
3rd Party Server
e.g. USGS

## Slide 30: Overcoming Semantic Heterogeneity
ODM Controlled Vocabulary System
  ODM CV central database
  Online submission and editing of CV terms
  Web services for broadcasting CVs
Variable Name
Investigator 1: | “Temperature, water”
Investigator 2: | “Water Temperature”
Investigator 3: | “Temperature”
Investigator 4: | “Temp.”
ODM VariableNameCV
Term
…
Sunshine duration
Temperature
Turbidity
…
From Jeff Horsburgh

## Slide 31
Dynamic controlled vocabulary moderation system
Local ODM
Database
Master ODM Controlled Vocabulary
ODM Website
ODM Controlled
Vocabulary Moderator
ODM Data Manager
ODM
Controlled Vocabulary
Web Services
ODM
Tools
Local
Server
XML
http://his.cuahsi.org/mastercvreg.html
From Jeff Horsburgh

## Slide 32: Thematic keyword search
Integration from multiple sources
Search on space and time domain
HydroDesktop – Data Access and Analysis

## Slide 33: HydroModeler
An integrated modeling environment based on the Open Modeling Interface (OpenMI) standard and embedded within HydroDesktop
Integrated modeling within a Hydrologic Information System: An OpenMI based approach, Castronova, A.M., Goodall, J.L., Ercan, M,B. Environmental Modelling & Software, In Press. 10.1016/j.envsoft.2012.02.011.

## Slide 34: Service Orientation of Hydrologic Models
A service-oriented modeling approach is needed to overcome platform dependencies, computer architecture requirements, or programming language incompatibilities that exist between models within an integrated software system.
Models are designed as web resources using the PyWPS implementation of the OGC WPS data specification on a RESTful web server.
Service orientation involves decomposing a larger software system into independent
distributed components. The client-server interaction (above) is very similar to the loose integration paradigm.
Client Wrapper – generic OpenMI component for wrapping web resources on-the-fly
WPS Services – models implemented as WPS resources
Models as web services using the Open Geospatial Consortium (OGC) Web Processing Service (WPS) standard, Castronova, A. M., Goodall, J. L., Elag, M.M. , Environmental Modelling & Software, In Review

## Slide 35
Integration with “R” Statistics Package

## Slide 36: A growing collection of HydroServers and community of users
Dry Creek Experimental Watershed (DCEW) (28 km2 semi-arid steep topography, Boise Front)
68 Sites
24 Variables
4,700,000+ values
Published by Jim McNamara, Boise State University
University of Maryland, Baltimore County
Montana State University
University of Texas at Austin
University of Iowa
Utah State University
University of Florida
University of New Mexico
University of Idaho
Boise State University
University of Texas at Arlington
University of California, San Diego
Idaho State University

## Slide 37: Open Development Model
http://hydrodesktop.codeplex.com
http://hydroserver.codeplex.com
http://hydrocatalog.codeplex.com

## Slide 38: General aspects of the approach
Storage in a community data model
Publication from a server
Data access through internet-based services using consistent language and format
Tools for access and analysis
Discovery through thematic and geographic search functionality
Integrated modeling and analysis combining information from multiple sources
Discovery and Integration
Data Services
Catalog
Synthesis and Research
Desktop/Client
Publication
Server
Metadata Services
Search Services
Standards
Information Model and Community Support Infrastructure
Accessibility
Discoverability
Consumability
Common functional components
The combination of these capabilities creates a common window on water observations data for the United States unlike any that has existed before.

## Slide 39: Looking to the Future
Move from prototype to operations
  Operational support of software and systems
  User support and training
  Repositories
  CUAHSI Data Center
Hydroshare
  An online, environment to be developed for the sharing of hydrologic data and models
  To expand data sharing capability of CUAHSI HIS
    Additional data classes
    Models, scripts, tools and workflows
    Collaboration/social networking
Community
  HIS has become bigger than one project
  Open Development Model to coordinate community contributions

## Slide 40: HydroShare
Visualization
Social Media
Data
Models
Data.gov
Earth
Exchange
HPC
CSDMS
CUAHSI
HydroServer
Create
Read
Update
Delete
WPS
HydroDesktop
Collaboration
Your favorite ...
Notes: HydroShare is a system that we have proposed to address these issues. It will be an online collaborative environment for sharing hydrologic data and models aimed at giving hydrologist the technology infrastructure they need to address critical issues related to water quantity, quality, accessibility, and management. HydroShare will expand the data sharing capability of the CUAHSI Hydrologic Information System by broadening the classes of data accommodated, expanding capability to include the sharing of models and model components, and taking advantage of emerging social media functionality to enhance information about and collaboration around hydrologic data and models. We plan to develop sustainable cyberinfrastructure, basically a website, for better access to water-related data and models in the hydrologic sciences. Social media functionality will help users be better informed of the use and value of data and models so as to discover the information and tools most relevant to their needs as well as stimulate the combination of data and coupling of models from multiple sources and catalyze sharing and collaboration. We envisage that the system will help hydrologists more easily access water-related research data and models that are online, retrieve them to their desktops, and perform analyses that could include accessing other models or using computing systems in the cloud or in distributed grid infrastructures. This project is funded from 2012-2017.
I have worked for 20+ years on hydrologic modeling and have codes that are widely used as well as that have died of neglect. I have also had projects whose data is nicely organized in CUAHSI HIS and others where the data is buried in private files. I would like to develop this system to do better.
HydroShare will be a social media based web site that provides access to hydrologic data and models. It will contain its own resources as well as links to external resources, e.g. web services from the USGS or CUAHSI HydroServers. It will interact with other data and modeling systems such as NASA earth exchange and provide easy to use access to HPC resources e.g. at CSDMS.
HydroShare will be directly accessible to serve as a portal for collaboration among hydrologists. We recognize that there are a lot of collaboration websites being developed, so will focus on providing hydrology value added functionality in terms of access to data and models. HydroShare will also have a web services interface, building on CUAHSI HIS that provides access from desktop software such as HydroDesktop and R.

## Slide 41: Can sharing data and models be as easy as sharing photos on Facebook or videos on YouTube?
Notes: In short, we would like to see if sharing hydrologic data and models can be as easy as sharing photos on Facebook or videos on YouTube.

## Slide 42: Can finding data and models be as easy as shopping on Amazon?
Items
Possible Filters
Available Formats
Recommendations
Prices (perhaps usage)
Notes: Or whether finding data and models can be as easy as shopping on Amazon, and perhaps not as heavy on your credit card.
List of items also includes other providers, aka not shipped by amazon.
List of data shows ‘facets’
,
Items show formats recommendations. Add-in shows pricetracking

## Slide 43
Sign In | Settings | Notifications | Feedback | Help
Dashboard
Recent Activity
My Content
View Your Resources
Explore
Discover Resources
Collaborate
Share with colleagues
Getting Started
What’s New
Provide feedback
HydroShare Blog
Developers
Partners
HydroShare Gallery
How HydroShare Works
Getting Started
CUAHSI
CUAHSI HIS
CUAHSI Water Data Center
Share and Collaborate
HydroShare is an online collaboration environment for sharing data, models, and code. Join the community to start sharing.
Terms of Use | Statement of Privacy| Copyright © 2012 CUAHSI
This material is based upon work supported by the National Science Foundation (NSF) under Grants No. OCI-1148453, OCI-1148090
Any opinions, findings, conclusions, or recommendations expressed in this material are those of the authors and do not necessarily reflect the views of the NSF.
HYDROSHARE
Notes: Home Page
Gallery – shows featured, new, or highly rated resources (data, code, models, workflows, etc.)
  Could have separate galleries for models, code, data, etc.
Top Bar Items
  Sign in
  Settings
    Create a HydroShare profile
    Choose display preferences
    Choose default privacy (share everything or choose what to share)
    Account information (password, etc.)
  Notifications - messages from the HydroShare team (choose to receive notifications from HydroShare)
  Help

## Slide 44
Dashboard
Recent Activity
My Content
View Your Resources
Explore
Discover Resources
Collaborate
Share with colleagues
Recent Activity
Profile
All activity | Only my activity
More
Jeff Horsburgh
Utah State University
jeff.horsburgh@usu.edu
Resources You May Like
You Should Follow
Announcements
People | Groups
Jeff Horsburgh
Utah State University
David Tarboton
Utah State University
Little Bear River ODM
Database 6/6/2012
View Details
Abstract: Time series of water quality sensor data in the Little Bear River, Utah, USA
Keywords: Temperature, Dissolved Oxygen, pH, Specific Conductance, Turbidity
What’s New at HydroShare: Click here to visit the HydroShare blog to learn more about recent updates and new HydroShare features.
Little Bear River Sites 6/6/2012
Little Bear River Excel File 6/6/2012
Watershed delineation Workflow 6/6/2012
Little Bear River SWAT Model
Shared by: David Tarboton
Little Bear River DEM
Shared by: David Tarboton
You are signed in as Jeff Horsburgh | Settings | Notifications | Feedback | Help
Terms of Use | Statement of Privacy| Copyright © 2012 CUAHSI
This material is based upon work supported by the National Science Foundation (NSF) under Grants No. OCI-1148453, OCI-1148090
Any opinions, findings, conclusions, or recommendations expressed in this material are those of the authors and do not necessarily reflect the views of the NSF.
HYDROSHARE
Notes: Dashboard
A user's home page
Shows user information/profile
Lists recent HydroShare activity in multiple categories (user's recent activity, all recent activity)
Announcements from HydroShare team
Suggests datasets the user might be interested in (geographic proximity, similar variables, similar time period, aggregations, keywords)
Suggests people that the user might want to "follow"
Suggests groups that the user might be interested in

## Slide 45: Architecture
HydroShare Portal
Browser Interface
Dashboard, Explore, Visualization, Modeling, Collaborate, Support
Service Interface
• Discovery API calls
• Create resource API
• Read resource API
• Update resource API
• Delete resource API
• Modeling API
R, MATLAB, HydroDesktop, ArcGIS, IDV, Python
Management Interface (Browser)
• Configure
• Set permissions
External Resource Interface
External Catalog (e.g. HydroCatalog)
External Data Sources
HPC Cluster
Authentication and Access control
Resource Catalog
External
Internal
Resource Store
Objects
Rules
Users
Visualization Tools
Modeling Tools
Social Media Data and information
Social Media
Discovery Tools
Resource Data Model
(Information about resources that are stored)
• Full metadata
• Data cart metadata
• Data discovery metadata
Data Model for Models
(Information Models and What it takes to run them on available compute resources)
• Many details to work out
Model Store
Model Metadata
Models
Desktop Compute Resources

## Slide 46: Questions ?
Summary
Simple and easy to use
Data and model sharing enabled by open standards based metadata
Find, create, share, connect, interact, work together online
Archive data collections accompanying research publications in easily accessible way
Integration and synthesis across data collections
To participate
See http://his.cuahsi.org
Join his@sdsc.edu
Write dtarb@usu.edu
Share
Your Resources
Explore
Discover Resources
Collaborate
Interact with colleagues
Terms of Use | Statement of Privacy| Copyright © 2012 CUAHSI
This material is based upon work supported by the National Science Foundation (NSF) under Grants No. OCI-1148453, OCI-1148090
Any opinions, findings, conclusions, or recommendations expressed in this material are those of the authors and do not necessarily reflect the views of the NSF.
You are signed in as David Tarboton | Settings | Notifications | Feedback | Help
HYDROSHARE