## Slide 1: Introduction to GAMS
Water Resources Planning and Management
Daene C. McKinney

## Slide 2: Introduction To GAMS
GAMS = General Algebraic Modeling System
GAMS Guide and Tutorials
  http://gams.com/docs/document.htm  Doc’s here
GAMS website
  www.gams.com
  http://gams.com/download/  Download here
McKinney and Savitsky Tutorials
  http://www.caee.utexas.edu/prof/mckinney/ce385d/Lectures/McKinney_and_Savitsky.pdf  Doc’s here

## Slide 3: Example Problem
Write a GAMS model and solve the following nonlinear program using GAMS

## Slide 4: Start GAMS
Start GAMS by selecting:
    Start  All Programs  GAMS  GAMSIDE

## Slide 5: Create New GAMS Project
Choose from the GAMSIDE:
    File  Project  New project

## Slide 6: Name New GAMS Project
In “My Documents”
Create a new directory by pressing the “folder” icon.
Name the new folder “Example”
Double click on “Example” folder
Type “Eq1” in the “File Name” box
Press Open

## Slide 7: New Project
The GAMS window should now show the new Eq1.gpr project window

## Slide 8: Create New GAMS Code File
Select: File  New
You should see the new file “Untitled_1.gms”

## Slide 9: Enter GAMS Code
The Model
The code
VARIABLES Z, X1, X2, X3;
EQUATIONS F ;
F.. Z =E= X1+2*X3+X2*X3-X1*X1-X2*X2-X3*X3 ;
MODEL HW41 /ALL/;
SOLVE HW41 USING NLP MAXIMIZING Z;
FILE res /HW41.txt/;
PUT res;
put "Solution X1 = ", put X1.L, put /;
put " X2 = ", put X2.L, put /;
put " X3 = ", put X3.L, put /;
Define Variables
Define Equations
Define Model
Solve Model
Write Output

## Slide 10: Enter GAMS Code
The Model
The code

## Slide 11: Run the Model
Select: File  Run, or Press the red arrow button

## Slide 12: GAMS Model Results
Results are in file:
  HW41.txt
Double Click this line to open results file

## Slide 13: Viewing Results File
Results
Note Tabs

## Slide 14: Another Example
How to determine the coefficients: Least Squares Regression
Model
Observation
Model
Residual

## Slide 15: Observations
t | x1(t) | x2(t) | x3(t) | y(t)
1 | 2 | 30 | 1 | 10
2 | 3 | 60 | 6 | 20
3 | 3 | 70 | 7 | 30
4 | 3 | 60 | 3 | 20
5 | 5 | 80 | 5 | 40
6 | 5 | 90 | 9 | 50
7 | 6 | 100 | 8 | 60
8 | 7 | 100 | 17 | 70

## Slide 16: Second GAMS Code
Define Variables
Define Equations
Define &
Solve Model
Write Output
Define Sets
& Data

## Slide 17: Results

## Slide 18: Results
Chart: time, t
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0
y(t)_hat | 10 | 20 | 30 | 20 | 40 | 50 | 60 | 70
y(t) | 10.21 | 26.53 | 24.45 | 20.48 | 41.52 | 43.03 | 55.82 | 75.56

## Slide 19: Capacity – Yield Example
Use linear programming in GAMS to derive a capacity-yield (K vs Y) function for a reservoir at a site having the following record of flows 5, 7, 8, 4, 3, 3, 2, 1, 3, 6, 8, 9, 3, 4, 9 units of flow.
Find the values of the capacity required for yields of 2, 3, 3.5, 4, 4.5, and 5.
Qt
K
St
Y
Rt
K
Y

## Slide 20: Capacity – Yield Curve
Qt
K
St
Y
Rt
K
Y

## Slide 21: Given a yield Y, what is the minimium capacity K we need?
Qt
Rt
K
St
Y
Y | K
1.0 | 
1.5 | 
2.0 | 
2.5 | 
3.0 | 
4.0 | 
Given
Find

## Slide 22: The GAMS Code

## Slide 23: Results: Yield = 5, Capacity = 14

## Slide 24: Results: Yield = 5, Capacity = 14
Capacity
Yield

## Slide 25: Capacity vs Yield Curve

## Slide 26: The DOLLAR Sign
S(t+1)$(ord(t) lt 15) + S('1')$(ord(t) eq 15) =e= S(t) + Q(t)- SPILL(t) - Y;
you can exclude part of an equation by using logical conditions ($ operator) in the name of an equation or in the computation part of an equation.
The ORD operator returns an ordinal number equal to
the index position in a set.

## Slide 27: Management of a Single Reservoir
2 common tasks of reservoir modeling:
Determine coefficients of functions that describe reservoir characteristics
Determine optimal mode of reservoir operation (storage volumes, elevations and releases) while satisfying downstream water demands

## Slide 28: Reservoir Operation
Compute optimal operation of reservoir given a series of inflows and downstream water demands
where:
St End storage period t, (L3);
St-1 Beginning storage period t, (L3);
Qt Inflow period t, (L3);
Rt Release period t, (L3);
Dt Demand, (L3); and
K Capacity, (L3)
Smin Dead storage, (L3)

## Slide 29: Comparison of Average and Dry Conditions

## Slide 30: GAMS Code
SCALAR K /19500/;
SCALAR S_min /5500/;
SCALAR beg_S /15000/;
SETS t / t1*t12/;
$include River1B_Q_Dry.inc
$include River1B_D.inc
$include River1B_Evap.inc
VARIABLES obj;
POSITIVE VARIABLES S(t), R(t);
S.UP(t)=K;
S.LO(t)=S_min;
These $include statements allow
Us to read in lines from other files:
Flows (Q)
Demands (D)
Evaporation (at, bt)
Capacity
Dead storage
Beginning storage
Set bounds on:
Capacity
Dead storage

## Slide 31: GAMS Code (Cont.)
EQUATIONS objective, balance(t);
objective..
obj =E= SUM(t, (R(t)-D(t))*(R(t)-D(t)) );
balance(t)..
(1+a(t))*S(t) =E=
(1-a(t))*beg_S $(ord(t) EQ 1) +
(1-a(t))*S(t-1)$(ord(t) GT 1) +
Q(t) - R(t)- b(t);
First Time, t = 1, t-1 undefined
After First Time, t > 1, t-1 defined
We’ll preprocess these

## Slide 32: $include Files
Parameter
Q(t) inflow (million m3)
* dry
/
t1 375
t2 361
t3 448
t4 518
t5 1696
t6 2246
t7 2155
t8 1552
t9 756
t10 531
t11 438
t12 343
/;
Parameter
D(t) demand (million m3)
/
t1 1699.5
t2 1388.2
t3 1477.6
t4 1109.4
t5 594.6
t6 636.6
t7 1126.1
t8 1092.0
t9 510.8
t10 868.5
t11 1049.8
t12 1475.5
/;
Parameter
a(t) evaporation coefficient
/
t1 0.000046044
t2 0.00007674
…
t11 0.000103599
t12 0.000053718/;
Parameter
b(t) evaporation coefficient
/
t1 1.92
t2 3.2
…
t11 4.32
t12 2.24/;
Flows (Q)
Demands (D)
Evaporation (at, bt)

## Slide 33: Results
 | Storage | Input | Release | Demand
t0 | 15000 |  |  | 
t1 | 13723 | 426 | 1700 | 1700
t2 | 12729 | 399 | 1388 | 1388
t3 | 11762 | 523 | 1478 | 1478
t4 | 11502 | 875 | 1109 | 1109
t5 | 12894 | 2026 | 595 | 595
t6 | 15838 | 3626 | 637 | 637
t7 | 17503 | 2841 | 1126 | 1126
t8 | 17838 | 1469 | 1092 | 1092
t9 | 18119 | 821 | 511 | 511
t10 | 17839 | 600 | 869 | 869
t11 | 17239 | 458 | 1050 | 1050
t12 | 16172 | 413 | 1476 | 1476
Chart: Month
| t1 | t2 | t3 | t4 | t5 | t6 | t7 | t8 | t9 | t10 | t11 | t12
Storage | 13723.26 | 12728.83 | 11762.29 | 11502.47 | 12894.05 | 15837.78 | 17503.44 | 17838.17 | 18118.57 | 17838.75 | 17239 | 16172.46
Release | 1699.5 | 1388.2 | 1477.6 | 1109.4 | 594.6 | 636.6 | 1126.1 | 1092 | 510.8 | 868.5 | 1049.8 | 1475.5
Inflow | 426 | 399 | 523 | 875 | 2026 | 3626 | 2841 | 1469 | 821 | 600 | 458 | 413